## Slide 1: Accelerator “Design By Modeling”
Tony Nowatzki

## Slide 2: Dark Silicon Problem
Esmaeilzadeh et al.
ISCA 2011
Core
Core
Core
Core
Cache
Under ITRS Scaling,
50% Dark Silicon
By 8 nm ?
Must Reduce or Use Dark Silicon!

## Slide 3: Multi Accelerator Design?
Core
Core
Core
Core
Cache

## Slide 4: Multi Accelerator Design?
Core
Core
Core
Core
Cache
A1
A2
A3
A1
A2
A3
A1
A2
A3
A1
A2
A3
Dark Silicon Solved?

## Slide 5: How to design accelerators?
Challenges
  General Purpose vs. Specialized?
  How do the interact with the core?
  What program features do they leverage?
  What hardware mechanisms to employ?
  How do we get the right set of acccelerators?

## Slide 6: Design in Vacuum
Super-Celerator
Mahlke Motors™
Speedup vs GPP | Super-Celerator |  |  | 
Application 1 | 3x |  |  | 
Application 2 | 9x |  |  | 
Application 3 | 1x |  |  | 
Geo Mean | 3x |  |  | 

## Slide 7: Design in Vacuum
Super-Celerator
Mahlke Motors™
Speedup vs GPP | Super-Celerator | SIMD | GPU | 
Application 1 | 3x | 4x | 1x | 
Application 2 | 9x | 2x | 100x | 
Application 3 | 1x | 1x | 1x | 
Geo Mean | 3x | 2x | 4.6x | 

## Slide 8: Design in Vacuum
Super-Celerator
Mahlke Motors™
Speedup vs GPP | Super-Celerator | SIMD | GPU | Tony-Celerator
Application 1 | 3x | 4x | 1x | 1x
Application 2 | 9x | 2x | 100x | 1x
Application 3 | 1x | 1x | 1x | 3x
Geo Mean | 3x | 2x | 4.6x | 1.4x

## Slide 9
Which Bins?
How to Design Accelerators?

## Slide 10: Our Approach: Design By Modeling
Find un-accelerated regions through use of models, and find patterns.
High-Level Design Proposal, and enumerate possible design decisions.
Explore the Design Space, and prune designs that don’t meet performance/energy goals
Iteratively Refine the Design, concretizing elements of the architecture incrementally

## Slide 11: Key: Transformable Dependence Graph
Represent programs as trace of micro-architectural events.
Transform this graph to model accelerators.

## Slide 12: Magic Version!
Lens
Profiler
Simulator (gem5)
Prism
F
D
F
D
F
D
F
D
F
D
F
D
F
D
F
D
F
D
F
D
F
D
F
D
F
D
F
D
F
D
F
D
F
D
F
D
F
D
F
D
F
D
F
D
F
D
F
D
F
D
F
D
F
D
F
D
F
D
Accelerator
Perf/Energy

## Slide 13: Step 1. Find Un-accelerated Regions
Func 1
Loop 1
Loop 2
Func 2
Func 3
Loop 3
Func 4
Accel 1
Accel 2
Accel 3
Application 1
Application 2
…
1.2x
0.5x
5x
1.1x
1x
1x
Best:
5x
1.1x
For this study:
  Un-accelerated: Performance < 1.3x Better than OOO
  73 Un-accelerated Regions Contribute 50% of Cycles
…

## Slide 14: Step 1. Find Un-accelerated Regions
Chart: 
| Mem. Latency | Loop Parallel + Irreg Mem. | Accel. Serialization | Other | Outer Loop | Short Function | Recursion
 | 20.83 | 22.29 | 23.32 | 7.77 | 18.22 | 5.65 | 1.02
SIMD +
Scatter/
Gather?
Simplest Possible Architecture?
Improve Current Accelerators?
New Accelerator?

## Slide 15: Program Structure Breakdown (by % of dynamic instructions)
Chart: 
| 164.gzip | 175.vpr | 181.mcf | 197.parser | 256.bzip2 | 401.bzip2 | 403.gcc | 429.mcf | 456.hmmer | 458.sjeng | 464.h264ref | cjpeg1 | cjpeg | conv | cutcp | djpeg1 | djpeg | fft | gsmdecode | gsmencode | h263enc | h264dec | h264enc | jpg2000dec | jpg2000enc | kmeans | lbm | merge | mm | mpeg2dec | mpeg2enc | mri-q | nbody | needle | nnw | radar | sad | spmv | stencil | tpacf | treesearch | vr | Average
Hot Trace | 0.24542 | 0.074762 | 0.57307 | 0.16279 | 0.18002 | 0.61808 | 0.12094 | 0.427 | 0.56174 | 0.21484 | 0.11716 | 0.3564 | 0.64124 | 0.91206 | 0.94008 | 0.67357 | 0.77828 | 0.35559 | 0.79661 | 0.8325 | 0.77518 | 0.17456 | 0.67971 | 0.55417 | 0.4782 | 0.623 | 0.30146 | 0.49871 | 0.88612 | 0.98602 | 0.061177 | 0 | 0.98699 | 0.68147 | 0.85174 | 0.99932 | 0.75863 | 0.98877 | 0.91262 | 0.92176 | 0.99993 | 0.10705 | 0.56687
Flat Inner Loop | 0 | 0.11261 | 0.21784 | 0.069181 | 0.066864 | 0.019855 | 0.006817 | 0.2755 | 0.049336 | 0.08502 | 0.012874 | 0.032015 | 0.12565 | 0.076092 | 0.030423 | 0.11938 | 0.12152 | 0.11791 | 0.10999 | 0.10143 | 0.16294 | 0.09497 | 0 | 0 | 0 | 0.16515 | 0.68251 | 0.49919 | 0.063229 | 0 | 0.5985 | 0 | 0.0077716 | 0.29375 | 0.024394 | 0.00048819 | 0.23698 | 0.0040307 | 0.03147 | 0.045081 | 6.1035e-05 | 0.42255 | 0.12103
Any Inner Loop | 0.0033107 | 0.034623 | 0.0018704 | 0.059644 | 0.069273 | 0.017909 | 0.13899 | 0.0047285 | 0.026557 | 0.27164 | 0.53938 | 0.0033443 | 0.0048477 | 0 | 0.0022103 | 0.031743 | 0.012335 | 0.046241 | 0.021589 | 0.0082404 | 0.00093824 | 0.14863 | 0.073263 | 0.040891 | 0.34852 | 0 | 0 | 0 | 0 | 0.012303 | 0 | 0.26981 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.05221
Any Loop | 0.74756 | 0.46335 | 0.20429 | 0.2483 | 0.34333 | 0.34267 | 0.2239 | 0.28538 | 0.20829 | 0.094232 | 0.052214 | 0.56676 | 0.21268 | 0.011717 | 0.023322 | 0.13529 | 0.057221 | 0.066415 | 0.022578 | 0.010331 | 0.054934 | 0.28187 | 0.063791 | 0.40263 | 0.03973 | 0.21183 | 0.014936 | 0 | 0.050287 | 0.0013771 | 0.031135 | 0.018516 | 0.0051811 | 0.024586 | 0.049787 | 0.00019079 | 0.0041415 | 0.007103 | 0.055883 | 0.033025 | 0 | 0.47029 | 0.14622
Direct Recursion | 0 | 0 | 0 | 0.17564 | 0 | 0 | 0.07212 | 7.8847e-07 | 0 | 0.022578 | 8.9414e-07 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0064367
Any Recursion | 0 | 0 | 0 | 0.081581 | 0 | 0 | 0.08282 | 0 | 0 | 0.31145 | 1.5602e-07 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 6.6502e-06 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.01133

## Slide 16: Step 2. High Level Design Proposal Nested Loop Accelerator (NLA)
For Simplicity, execute only loop structures in the accelerator.
For efficiency, execute with compound functional units.
CFU
ALU
MEM
MPY

## Slide 17: Step 2. High Level Design Proposal Nested Loop Accelerator (NLA)
BB1
BB2
BB3
BB4
BB4
BB3
BB4
BB4
BB5
Nested Loop
Dynamic Basic Block Trace

## Slide 18: Step 2. High Level Design Proposal Nested Loop Accelerator (NLA)
BB1
BB2
BB3
BB4
BB4
BB3
BB4
BB4
BB5
CPU
NLA
CPU
Transfer Register
State &
Configure NLA
Transfer Back
Register State
Dynamic Basic Block Trace

## Slide 19: Step 2. High Level Design Proposal Nested Loop Accelerator (NLA)

## Slide 20: Step 3. Design Space Exploration
NLA Design | Practicality | Details
Sequential | Extremely Simple | Each CFU Executes Sequentially Centralized Unit Controls Execution
Pipelined | Practical | CFUs execute in pipelined fashion Central unit manages data deps.
Decoupled | Practical, Needs Design | CFUs execute in dataflow fashion Distributed Issue Queues Software helps disambiguate memory
Speculative OOO | Somewhat Impractical | Speculative Execution w/ Recovery Memory Dependence Prediction

## Slide 21: Consider This Architecture
GPP
Core
DySER
SIMD
C-Cores
BERET
NLA

## Slide 22: Preliminary Results
Chart: Speedup Relative to 4-Issue OOO GPP
| cutcp | mm | nnw | merge | tpacf | lbm
SIMD (8x32 bit Vec) | 4.96 | 4.12 | 1.76 | 1 | 1 | 1
DySER (8x32 bit Vec) | 1.89 | 5.14 | 1.77 | 2.21 | 0.6 | 0.59
BERET | 0.25 | 0.33 | 0.32 | 1 | 1 | 1
Ccores | 0.31 | 0.33 | 0.32 | 0.76 | 0.45 | 0.35
NLA-SEQ | 0.24 | 0.3 | 0.3 | 0.73 | 0.2 | 0.23
NLA-Pipelined | 0.34 | 0.6 | 0.51 | 1.68 | 0.42 | 0.51
NLA-Decoupled | 0.73 | 0.83 | 0.73 | 2.25 | 1.19 | 2.76
NLA-Speculative-OOO | 3.39 | 2.41 | 1.99 | 4.13 | 1.79 | 3.43
NLA Definitely Ineffective
NLA Probably Ineffective
NLA Probably Effective

## Slide 23: Step 4: Iteratively Refine Design (Design Everything Else…)
Internal Buffering
Specifics of Interconnection Network
Token Passing Protocol
Mechanism for enforcing memory dependence
Preventing Deadlock
Exception Handling

## Slide 24: Conclusions
Design By Modeling
  Helps find unexplored opportunities
  Iterative TDG modeling based design
Nested Loop Accelerator
  Potentially new acceleration domain
  Decoupled design looks like a promising target for further exploration